## Slide 1: OSPF

## Slide 2: OSPF
Open Shortest Path First or OSPF protocol is an intradomain routing protocol based on link state routing.
To handle routing efficiently and in a timely manner, OSPF divides an autonomous system into areas.
An area is a collection of networks, hosts, and routers all contained within an autonomous system.
An autonomous system can be divided into many different areas. All networks inside an area must be connected.

## Slide 3
Routers inside an area flood the area with routing information.
At the border of an area, special routers called area border routers summarize the information about the area and send it to other areas.
Among the areas inside an autonomous system is a special area called the backbone; all the areas inside an autonomous system must be connected to the backbone.
The routers inside the backbone are called the backbone routers.

## Slide 4
Each area has an area identification. The area identification of the backbone is zero. Figure 22.24 shows an autonomous system and its areas.

## Slide 5: Path vector routing
Distance vector and link state routing are both intradomain routing protocols. They can be used inside an autonomous system, but not between autonomous systems.
Both of these routing protocols become intractable when the domain of operation becomes large.
Distance vector routing is subject to instability if there are more than a few hops in the domain of operation.
Link state routing needs a huge amount of resources to calculate routing tables. It also creates heavy traffic because of flooding.

## Slide 6
In path vector routing, we assume that there are some nodes in each autonomous system that acts on behalf of the entire autonomous system called speaker nodes.
The speaker node in an AS creates a routing table and advertises it to speaker nodes in the neighboring ASs.
The idea is the same as for distance vector routing except that only speaker nodes in each AS can communicate with each other.
However, what is advertised is different. A speaker node advertises the path, not the metric of the nodes, in its autonomous system or other autonomous systems.

## Slide 7
Initialization
At the beginning, each speaker node can know only the reachability of nodes inside its autonomous system.
Figure 22.30 shows the initial tables for each speaker node in a system made of four ASs.
Node A1 is the speaker node for AS1,
B1 for AS2, C1 for AS3, and D1 for AS4.
Node A1 creates an initial table that shows Al to A5 are located in ASI and can be reached through it.
Similarly other speaker nodes will create those initial tables.

## Slide 8
Sharing
  Just as in distance vector routing, in path vector routing, a speaker in an autonomous system shares its table with immediate neighbors.
  In Figure 22.30, node Al shares its table with nodes Bl and Cl. Node Cl shares its table with nodes Dl, Bl, andAl. Node Bl shares its table with Cl andAl. Node Dl shares its table with Cl.
Updating
  When a speaker node receives a two-column table from a neighbor, it updates its own table by adding the nodes that are not in its routing table and adding its own autonomous system and the autonomous system that sent the table.
  After a while each speaker has a table and knows how to reach each node in other ASs.
  According to the figure, if router A1 receives a packet for node A3, it knows that the path is in AS1 (the packet is at home);
  but if it receives a packet for D1, it knows that the packet should go from AS1, to AS2, and then to AS3.
  The routing table shows the path completely. On the other hand, if node Dl in AS4 receives a packet for node A2, it knows it should go through AS4, AS3, and AS 1.

## Slide 9
  Figure 22.31 shows the tables for each speaker node after the system is stabilized.

## Slide 10
According to the figure, if router Al receives a packet for nodes A3, it knows that the path is in ASI (the packet is at home);
but if it receives a packet for Dl, it knows that the packet should go from ASl, to AS2, and then to AS3. The routing table shows the path completely.
On the other hand, if node Dl in AS4 receives a packet for node A2, it knows it should go through AS4, AS3, and AS 1.

## Slide 11: BGP
Border Gateway Protocol (BGP) is an interdomain routing protocol using path vector routing. It first appeared in 1989.
We can divide autonomous systems into three categories: stub, multihomed, and transit.
  Stub AS: - A stub AS has only one connection to another AS.
  The hosts in the AS can send data traffic to other ASs.
  The hosts in the AS can receive data coming from hosts in other ASs.
  Data traffic, however, cannot pass through a stub AS.
  A stub AS is either a source or a sink.
  A good example of a stub AS is a small corporation or a small local ISP.

## Slide 12
A multihomed AS has more than one connection to other ASs, but it is still only a source or sink for data traffic.
It can receive data traffic from more than one AS. It can send data traffic to more than one AS, but there is no transient traffic.
It does not allow data coming from one AS and going to another AS to pass through.
A good example of a multihomed AS is a large corporation that is connected to more than one regional or national AS that does not allow transient traffic.

## Slide 13
Transit AS. A transit AS is a multihomed AS that also allows transient traffic.
Good examples of transit ASs are national and international ISPs (Internet backbones).

## Slide 14
Path attributes
  In path vector routing, path information is stored in routing tables and corresponds to that path there’s some specific information associated.
  In order to show that information there are some attributes defined.
  Each attribute gives some information about the path.
  The list of attributes helps the receiving router make a more-informed decision when applying its policy.
  Attributes are divided into two broad categories: well known and optional.
    A well-known attribute is one that every BGP router must recognize.
    An optional attribute is one that needs not be recognized by every router.

## Slide 15
BGP Sessions:
The exchange of routing information between two routers using BGP takes place in a session.
A session is a connection that is established between two BGP routers only for the sake of exchanging routing information.

## Slide 16
Types of BGP Sessions
  External and Internal BGP